## Slide 1: Piraeus University of Applied Sciences Department of Computer Systems Engineering
Introduction to Automatic Control Systems
Anastasia Veloni

## Slide 2: What is Automatic control theory?
A field of knowledge which explores the possibilities of reducing or eliminating the human role in the activities connected with controlling of various physical objects.

## Slide 3
Why automatic control is important?
Automatic control is essential in any field of engineering and science.
Automatic control is an important and integral part of space-vehicle systems, robotic systems, modern manufacturing systems, and any industrial operations.
The reasons for automation of process plants are to provide safety and at same time maintain desired product quality and reduce demand on human labor.
It is desirable that most engineers and scientists are familiar with theory and practice of automatic control.

## Slide 4: GOALS FOR LEARNING
Given a control system, Identify the system components and their function.
Given a variable to be controlled, Determine the structure of a system that will control that variable.
Given a control system design problem, To appreciate and understand that the complexity of most systems makes it difficult to predict their behavior.

## Slide 5: Required Knowledge
Linear algebra
Vectors and matrices
Complex numbers
Basic Physics
Linear systems and signals
Laplace and Z Transform
Software for control systems analysis and design

## Slide 6
A system takes a signal as an input and transforms it into another signal
system
input
output
System
  Visual representation of a system

## Slide 7: Example: An Electrical Circuit System
Simulink representation of the electrical circuit
+
-
i
vc
vs
R
C
vs(t)
vc(t)
first order
system
vs, vc
t

## Slide 8: What is a control system?
Generally speaking, a control system is a system that is used to realize a desired output or objective.
Control systems are everywhere
  They appear in our homes, in cars, in industry, in scientific labs, and in hospital.

## Slide 9: The central heating system in a house

## Slide 10: A machine tool

## Slide 11: A brief history of control
Ctesibius's water clock (159 BC)
Water drips from the higher container to the lower container.
As the water level rises in the lower container, it raises the float on the surface of the water.
The float is connected to a stick with notches, and as the stick rises, the notches turn a gear, which moves the hand that points to the time.

## Slide 12: A brief history of control
When the load of the engine increases, its speed decreases, then the governor increases the supply of fuel & vice-versa in case of decrease of load.
Fly-ball governor (James Watt,1769)
The Invention That Changed The World
A governor is a feedback design on a machine or engine used to provide automatic control, as of speed, pressure or temperature
A fly-ball governor is a specific type of governor, that controls the speed of an engine, by regulating the fuel admitted.

## Slide 13
Birth of mathematical control theory
  G. B. Airy (1840)
    the first one to discuss instability in a feedback control system
    the first to analyze such a system using differential equations
  J. C. Maxwell (1868)
    the first systematic study of the stability of feedback control
  E. J. Routh (1877)
    deriving stability criterion for linear systems
  A. M. Lyapunov (1892)
    deriving stability criterion that can be applied to both linear and nonlinear differential equations

## Slide 14
Birth of classical control design method
  H. Nyquist (1932)
    developed a relatively simple procedure to determine stability from a graphical plot of the loop-frequency response.
  H. W. Bode (1945)
    frequency-response method
  W. R. Evans (1948)
    root-locus method
With the above methods, we can design control systems that are stable, acceptable but not optimal in any meaningful sense.

## Slide 15
  Late 1950s: designing optimal systems in some meaningful sense
  1960s: digital computers help time-domain analysis of complex systems, modern control theory has been developed to cope with the increased complexity of modern plants
  1960s~1980s: optimal control of both deterministic and stochastic systems; adaptive control and learning control
  1980s~present: robust control, H-infinity methods ( H∞) are used in control theory to synthesize controllers achieving stabilization with guaranteed performance.
Development of modern control design

## Slide 16: Control = Sensing + Computation + Actuation
Sense
Vehicle Speed
Compute
Control “Law”
Actuate
Gas Pedal
In Feedback “Loop”
Goals
  Stability: system maintains desired operating point.
  Performance: system responds rapidly to changes.
  Robustness: system tolerates perturbations in dynamics.

## Slide 17: Types of Control System
Control Systems
Natural
Man-made
Manual
Automatic
Open-loop
Closed-loop
Non-linear
linear
Time variant
Time invariant
Non-linear
linear
Time variant
Time invariant

## Slide 18: Types of Control System
  Room Temperature regulation Via A.C
  Human Body Temperature Control
  Room Temperature regulation Via Electric Fan
  Water Level Control

## Slide 19
Example of a Manual Control System
A manual control system for regulating the level of fluid in a tank by adjusting the output valve.
The operator views the level of fluid through a port in the side of the tank.
The reference is a desired level of fluid that operator is instructed to maintain.
The actuator is the valve that opens or closes the fluid flow out.
The sensor is visual.
The controller is the operator.

## Slide 20: Manual Open Loop Diagram
Tap Handle
Valve
Water level
Water
Flood

## Slide 21: Manual Closed Loop Diagram
Tap Handle
Valve
Water level
Water
Eyes / Brain
Hand
Correct level

## Slide 22: Automatic Closed Loop Diagram
Start Switch
Valve
Water level
Water
Level Sensor
Control Unit
Correct level
Press

## Slide 23: Classification of control systems
According to structure
Open-loop control
Closed-loop control
Composition control
Open-loop＋Closed-loop＝Composite control system

## Slide 24
An open-loop system cannot self-correct any errors it could make when the preset value drifts.
Controller
Output
Input
Process
Open-Loop Control System
Note that any control systems that operates on a time basis are open-loop.
In an open-loop control system the output is neither measured nor “fed back” for comparison with the input.

## Slide 25
Practical Examples of Open Loop Control Systems
Electric Hand Drier – Hot air (output) comes out as long as you keep your hand under the machine, irrespective of how much your hand is dried.
Automatic Washing Machine – This machine runs according to the pre-set time irrespective of washing is completed or not.
Bread Toaster - This machine runs as per adjusted time irrespective of toasting is completed or not.
Automatic Tea/Coffee Maker – These machines also function for pre adjusted time only.
Timer Based Clothes Drier – This machine dries wet clothes for pre – adjusted time, it does not matter how much the clothes are dried.
Light Switch – lamps glow whenever light switch is on irrespective of light is required or not.
Volume on Stereo System – Volume is adjusted manually irrespective of output volume level.

## Slide 26
Hero’s of Alexandria
Temple doors
Heron designed an automatic temple door opener, which used heat and pneumatics to open a set of temple doors.
To open the doors, the priest lit a fire on the altar, heating the air within and causing it to expand.
This expansion in volume forced water out of the sphere and into the bucket, which moved downwards under the extra weight.
This bucket was connected to a rope coiled around a spindle and, as the bucket moved downwards, this spindle revolved, making the doors open.
(c. 10 CE - c. 70 CE)

## Slide 27
Depending upon the amount of clothes or how wet they are, a user would set a timer (controller) to say 30 minutes and at the end of the 30 minutes the drier will automatically stop and turn-off even if the clothes are still wet or damp.
  Open loop drying system

## Slide 28
Open loop Control of the speed of a turntable

## Slide 29: Open-Loop Control System
Missile Launcher System
The control system consists of potentiometer, power amplifier, motor, gearing between the motor and missile launcher, and the missile launcher.
The input is the desired angular position of the missile launcher.

## Slide 30: A microwave oven
Timer
Magnetron
Electrical energy
Heat, Light, Hot food
On/Off
Turntable
Food
1st Inputs
2nd Subsystems
3rd Boundary
4th Flow of information arrows
5th outputs
Set time

## Slide 31: Some comments on open-loop control systems
  Simple construction and ease of
  maintenance.
  Less expensive than a closed-loop system.
  No stability problem.
  Recalibration is necessary from time to time.
  Sensitive to disturbances.

## Slide 32: When should we apply open-loop control?
  The relationship between the input and output is exactly known.
  There are neither internal nor external disturbances.
  Measuring the output precisely is very hard or economically infeasible.

## Slide 33
Controller
Output
Input
Process
Comparator
Measurement
Closed-Loop Control System
A closed-loop control system measures the value of the parameter being controlled at the output of the system and compares this to the desired value.
The term feedback is used to refer to a situation in which two (or more) dynamical systems are connected together such that each system influences the other and their dynamics are strongly coupled.

## Slide 34: Closed Loop Control System
Sensor
Actuator
Process
Controller
+
+
Set-point or Reference input
Actual Output
Error
Controlled Signal
Disturbance
Manipulated Variable
Feedback Signal
+
-
+
+
comparison component :
its output equals the algebraic sum of all input signals.

## Slide 35: Basic components of a control system
Plant
Controlled Variable
Expected Value
Controller
Actuator
Sensor
Disturbance

## Slide 36: Basic concepts of a control system
Plant
1.Plant: a physical object to be controlled such as a mechanical device, a heating furnace, a chemical reactor or a spacecraft.
Controlled
variable
2.Controlled variable: the variable controlled by Automatic Control System , generally refers to the system output.
Expected
value
3.Expected value : the desired value of controlled variable based on requirement, often it is used as the reference input.
Notes: .

## Slide 37
Disturbance
7.Disturbance: the unexpected factors disturbing the normal functional relationship between the controlling and controlled parameter variations.
Controller
4.Controller: a hardware device or a software program that can calculate the required control signal.
Actuator
5.Actuator: a mechanical device that takes energy, usually created by air, electricity, or liquid, and converts that into some kind of motion.
Sensor
6.Sensor : a device that measures a physical quantity and converts it into a signal which can be read by an observer or by an instrument.

## Slide 38: What is a Controller?
A controller is a device that generates an output signal based on the input signal it receives.
The input signal is actually an error signal, which is the difference between the measured variable and the desired value, or set point.
This input error signal represents the amount of deviation between where the process system is actually operating and where the process system is desired to be operating.

## Slide 39: Structure of a Controller
The controller provides an output signal to the final control element, which adjusts the process system to reduce this deviation.
Deviation is the difference between the set point of a process variable and its actual value. This is a key term used when discussing various modes of control.
The characteristic of this output signal is dependent on the type, or mode, of the controller.

## Slide 40: PID Controller
PID controller is a generic name for a controller containing a linear combination of
Propotional (P)
Integral (I)
Derivative (D)
terms acting on a control error.
An ideal PID controller is described by the control law

## Slide 41: Proportional Control in Action
  Increasing gain approaches setpoint faster
  Can leads to overshoot, and even instability.
  Steady-state offset.

## Slide 42: Derivative Control in Action
  Damping fights oscillation and overshoot.
  But it’s vulnerable to noise.

## Slide 43: PID Control in Action
  But, good behavior depends on good tuning!

## Slide 44: The effects of the increasing each of the controller parameters are:
The time for the plant output to rise beyond 90% of the desired level for the first time.
How much the peak level is higher than the steady state.
The time it takes for the system to converge to its steady state.
The difference between the steady state output and the desired output.

## Slide 45: Time response of a 2nd order system

## Slide 46: Industrial PID controllers

## Slide 47
Examples of feedback control systems:
  Temperature control using a room heater

## Slide 48
The driver uses the difference between the actual and the desired direction of travel to generate a controlled adjustment of the steering wheel.
  Automobile steering control system
Typical direction
of
travel response.

## Slide 49: Cruise control in a car
Cruise control (sometimes known as speed control) is a system that automatically controls the speed of a motor vehicle. The system is a servomechanism that takes over the throttle of the car to maintain a steady speed as set by the driver.

## Slide 50
A controller is a computer in the car, measuring speed and desired speed, and sends command signals (desired torque) to the engine.

## Slide 51
Closed loop control of the speed of a turntable
error

## Slide 52: Missile Launcher System
This potentiometer feeds a signal back to the difference amplifier.
Should an error exist, it is amplified and applied to a motor drive which adjusts the output-shaft position until it agrees with the input-shaft position and the error is zero.

## Slide 53
Antenna azimuth position control system:
a. system concept
b. detailed layout
The purpose of this system is to have the azimuth angle output of the antenna , follow the input angle of the potentiometer.

## Slide 54
Antenna azimuth position control system:
c. schematic
d. functional block diagram
The input command is an angular displacement.
Similarly, the output angular displacement is converted to a voltage by the potentiometer in the feedback path.
The signal and power amplifiers boost the difference between the input and output voltages. This amplified actuating signal drives the plant.
The potentiometer converts the angular displacement into a voltage.
When the input and output match, the error will be zero, and the motor will not turn.

## Slide 55: Flush toilet
Lever
Water Tank
Float
Piston
lever
Plant
Controller
Actuator
Sensor

## Slide 56: Block Diagram for the water level control system
amplifier
Motor
Gearing
Valve
Actuator
Water
container
Process
controller
Float
measurement (Sensor)
Error
Feedback signal
resistance comparator
Desired
water level
Input
Actual
water level
Output

## Slide 57: Open-loop vs. closed-loop
Open-loop control
Closed-loop control
Simple structure,
low cost
Low resistance to disturbance
Easy to regulate
Ability to correct error
Complex structure,
high cost
High
resistance of disturbance
Selecting parameter is critical (may cause stability problem)
Notes: .

## Slide 58: Classification of control systems
According to reference input
Constant-value control
Servo/tracking control
Programming control
the reference input (expected value) is a constant value
the controller works to keep the output around the constant value
e.g. constant-temperature control, liquid level control and constant-pressure control.
the reference input may be unknown or varying
the controller works to make the output track the varying reference
e.g. automatic navigation systems on boats and planes, satellite-tracking antennas
the input changes according to a program
the controller works according to predefined command
e.g. numerical control machine

## Slide 59
Servo System
A Servo System (or servomechanism) is a feedback control system in which the output is some mechanical position, velocity or acceleration.
Antenna Positioning System
Modular Servo System (MS150)

## Slide 60: A demonstration robot containing several servo motors

## Slide 61: Classification of control systems
According to system characteristics
Linear control system
Nonlinear control system
superposition principle applies
described by linear differential equation
described by nonlinear differential equation

## Slide 62
Linear vs. Nonlinear Control System
A Control System in which output varies linearly with the input is called a linear control system.
output has nonlinear relationship
output has linear relationship

## Slide 63
Inverted pendulum
Inverted pendulum system is a nonlinear unstable system , an ideal experiment platform for teaching control theories and conducting various control experiments.
The pendulum is controlled to remain upright by a feedback controller.
The controller receives system state information from sensors, and performs calculations for the control signal that is sent to an actuator to control the pendulum.

## Slide 64
Examples of real systems that behave as inverted pendulums
Rocket MAXUS 1 in starting position
Segway Personal Transporter, a self-balancing vehicle

## Slide 65: Classification of control systems
According to signal form
Continuous control system
Discrete control system
All the signals are functions of continuous time variable t
Signals are in the form of either a pulse train or a digital code

## Slide 66
Computer Control System
A/D
D/A
computer
Controlled
process
feedback
r(t)
c(t)
e(t)
－
e*(t)
u*(t)
u (t)
Reference input: The ideal or desired output of the system.
Process: The system or subsystem, which is controlled by the closed-loop system.
Digital-to-Analog Converter (D/A): A device that converts a digital signal into an analog signal.
Analog-to-Digital Converter (A/D): A device that converts an analog signal into a digital signal, usually a numerically coded signal.

## Slide 67
Signal Forms in a Digital Control System
(Sampled data system)
Sample-and-Hold (S/H):
A circuit that receives an analog input signal and holds this signal at a constant value for a specified period of time.
    Transducer: A device that converts an input signal into an output signal of another form (converting a pressure signal into a voltage output).

## Slide 68
Computer controlled system (CCS)
The controller: Computes the error signal (or the difference) and generates an appropriate input signal to the controlled process in order to provide the desired output signal.
Using the controller, a transfer function is being implemented, the design of which can be made via a suitable algorithm that is programmed into the PC or by using special equipment.
The computer may be a digital filter or a microprocessor, depending on the complexity and size of the system.

## Slide 69: Digital Control of hot air blower – system interfaced with digital computer for control purpose
The information regarding the measured value of air temperature is obtained in the form of analog signal.
An ADC is used to convert the analog signal into digital signal before it is fed to the computer.
The status of fully open or fully closed position of the fan inlet valve is obtained in the form of digital signals.
For the output generated by the computer, DAC is used to send control signal in analog form to the motor control.

## Slide 70: Computer control of Aircraft turbojet engine
The control requires feedback of the engine state (speed, temperature and pressure), measurements of the aircraft state (speed and direction) and pilot command.

## Slide 71: Closed-Loop Drug Delivery System
A sensor is utilized to measure the levels of the regulated drug or nutrient in the blood.
This measurement is converted to digital form and fed to the control computer, which drives a pump that injects the drug into the patient’s blood.

## Slide 72
ADVANTAGES OF DIGITAL CONTROL SYSTEMS AND APPLICATIONS
Great flexibility in modifying the controller’s features that can easily be altered by modifying the program.
Data processing is easy. Complex calculations can be performed easily and quickly.
They present better technical behavior in comparison to the analog control systems in terms of reliability and sensitivity to disturbances.
They have an improved stability, a lower physical weight and, in many cases, a lower implementation cost.

## Slide 73
DISADVANTAGES
OF DIGITAL CONTROL SYSTEMS
The errors introduced during both the sampling process of continuous systems, and the quantization of discrete-time signals.
The difficulty in the digital control system design, if the process is complicated.
In the digital control of a complex process, the designer must have a good knowledge of the process to be controlled and should be able to obtain its corresponding mathematical model.

## Slide 74: Classification of control systems
According to parameters
Time-invariant system
Time-varying system
The parameters of a control system are stationary with respect to time
System contain elements that drift or vary with time

## Slide 75
Deterministic vs. Stochastic Control System
A control System is deterministic if the response to input is predictable and repeatable.
If not, the control system is a stochastic control system.
y(t)
t
x(t)
t
z(t)
t

## Slide 76
Multivariable Control System
Desired Output Response
Measurement
Output Variables
Controller
Process
Multi Input - Multi Output (MIMO) System

## Slide 77
Process Industry – Boiler generator
Control used to regulate level, pressure and pressure of refinery vessel

## Slide 78: Adaptive Control System
The dynamic characteristics of most control systems are not constant for several reasons.
The effect of small changes on the system parameters is attenuated in a feedback control system.
An adaptive control system is required when the changes in the system parameters are significant.

## Slide 79: Learning Control System
A control system that can learn from the environment it is operating is called a learning control system.

## Slide 80: The control system design process
1. Establish control goals
2. Identify the variables to control
3. Write the specifications
for the variables
4. Establish the system configuration
Identify the actuator
5. Obtain a model of the process,
the actuator and the sensor
6. Describe a controller and select
key parameters to be adjusted
7. Optimize the parameters and
analyze the performance
Finalize the design
Performance does not
meet the specifications
Performance
meet the
specifications

## Slide 81: System Modeling
Purpose of models in control systems:
  The mathematical model of a system is the basis for all control system analysis and design methods.
Mathematical models of the control systems are the mathematical relationships between the system’s variables.
  A detailed model allows some verification of the performance of the control system through simulation, before it is implemented on the actual system.

## Slide 82: Types of Models
Physical Models
  scale models
  analogue models
Mathematical Models
  analytically based
  experimentally based
A model for a given system depends upon:
defined system boundaries
objective of the study
level of approximation required

## Slide 83
Mathematical models of
control systems
1) Differential equations
2) Transfer function
3) Block diagram
4) Signal flow graph
5) State variables (modern control theory)

## Slide 84
Examples
1) Differential equations

## Slide 85: Example : A mechanism
Define: input → F ，output → y. We have:

## Slide 86: Transfer Function
Transfer Function is the ratio of Laplace transform of the output to the Laplace transform of the input.
Plant
y(t)
u(t)

## Slide 87: LAPLACE TRANSFORM
Laplace transform is a mathematical tool particularly suitable for the study and design of LTI systems.
LTI systems are usually described by linear differential equations with constant coefficients.
Laplace transform converts a linear differential equation with constant coefficients to an algebraic equation.

## Slide 88
Examples
2) Transfer function

## Slide 89
Example : A RC circuit

## Slide 90: Block Diagram
Block diagrams are used as schematic representations
of mathematical models.
The various pieces correspond to mathematical entities.
Can be rearranged to help simplify the equations used
to model the system.

## Slide 91: Examples
3) Transfer function - The water level control system

## Slide 92
Example :Displacement control system of a hydraulic amplifier

## Slide 93
Example :Displacement control system of a hydraulic amplifier
The equations that describe the displacement-control system of the hydraulic amplifier are

## Slide 94
We apply Laplace transform to the system equations, assuming zero initial conditions, and we plot the block diagram of the system.

## Slide 95: 4) Signal flow graph
Signal flow graphs display the transmission of signals through the system, as does the block diagrams, but it is easier to draw and easier to manipulate than the block diagrams.
Alternative method to block diagram representation, developed by Samuel Jefferson Mason.
A signal-flow graph consists of a network in which nodes are connected by directed branches.

## Slide 96: Example: From Block Diagram to Signal-Flow Graph Model

## Slide 97: Example: From System to Signal-Flow Graph Model

## Slide 98
5) State variables
In control engineering, a state space representation is a mathematical model of a physical system as a set of input, output and state variables related by first-order differential equations.
We group these first-order equations using a compact matrix notation in a model known as the state variable model.
The state variable differential equation
The output equation

## Slide 99: Example: RLC circuit
The state-space representation of the system is

## Slide 100: Example: RLC circuit
The state-space representation of the system is

## Slide 101: Example: Hydraulic system
The state equations that describe the system are

## Slide 102: Control System Design
Define the control system objectives.
Identify the system boundaries.
  define the input, output and disturbance variables
Determine a mathematical model for the components and subsystems.
Combine the subsystems to form a model for the whole system.
Choose of a suitable controller so that closed performance meets the specifications.
Use methods and techniques for analysis and design.

## Slide 103: Methods and Techniques?
Stability analysis. Stability criteria.
Analysis of ACS in time (root locus) and frequency domain (Nyquist, Bode, Nichols).
Stability of ACS in frequency domain (gain margin, phase margin, Nyquist criteria).
Second order systems- Steady state and transient specifications (sensitivity, rise time, settling time, overshoot etc.)

## Slide 104: Control Tools
Modeling
  Input/output representations for subsystems + interconnection rules
  System identification theory and algorithms
  Theory and algorithms for reduced order modeling + model reduction
Analysis
  Stability of feedback systems, including robustness “margins”
  Performance of input/output systems (disturbance rejection, robustness)
Synthesis
  Constructive tools for design of feedback systems
+ SIMULATION TOOLS

## Slide 105: SIMULATION
A computer simulation is a computer program that attempts to simulate an abstract model of a particular system.
A model is a schematic description of a system and can be used for further study of its characteristics.
System modeling is the procedure of expressing a (usually) simplified version of the system in terms of differential equations.

## Slide 106: The simulation procedure is implemented in the following steps:
The problem and the study procedure are specified.
The mathematical model of the system is derived.
A suitable simulation software is selected.
Simulation tests are run and are compared with the real system (if available).
Extensive simulations are run and the results are analyzed.

## Slide 107: Software for Modeling and Simulating control systems
MATLAB is a Mathworks product. It is a very popular software tool designed for scientific and engineering computing. It comes with a control systems toolbox, a toolbox that provides a way for systematically analyzing, designing, and tuning linear control systems.
Simulink is also a Mathworks product. It provides an interactive graphical environment and a set of block libraries that let you design, simulate, implement, and test a variety of time-varying systems.
Program CC is a Systems Technology product. It provides a control system design package containing many tools and algorithms of current control system theory and practice.

## Slide 108: Simulation tools:
SIMAPP is another computer simulation software for modeling systems in the time and frequency domains. The model is built visually through block diagrams.
LabVIEW uses the technique of graphical programming. This type of coding is referred to as G-Code (for graphical code). The program developed by National Instruments is widely used in industry for a variety of applications. When using LabVIEW many settings of the instruments can be changed remotely instead of manually.
SCILAB is an open-source software similar to MATLAB. It comes with toolboxes appropriate for the simulation, design, and optimization of control systems.

## Slide 109: Simulation tools
SIMVIEW is a set of freely available simulators in the area of control engineering. The simulators are developed in LabVIEW. The simulators can be used without LabVIEW being installed, but in that case the freely available LabVIEW Run-Time Engine must be installed.
CODAS is an application for Control System Design using a Multiple Document Interface (MDI) which allows an arbitrary number of child windows to be created. In each child window the behaviour of a system may be examined in different ways.
VisSim is a Windows-based program for the modeling and simulation of complex dynamic systems. VisSim combines a drag-and-drop block diagram interface with a powerful mathematical engine that offers a simple method for constructing, modifying and maintaining complex system models.
.

## Slide 110: Simulation tools
DYMOLA is a complete tool for modeling and simulating integrated and complex systems. It is used in automotive, aerospace, energy, robotics, packaging, process and other industries. Dymola is based on the Modelica open standard, an object-oriented multi-domain language for component-oriented modeling of complex systems.
Simscape enables to create models of physical systems within the Simulink environment. With Simscape, we build physical component models based on physical connections. Simscape helps to develop control systems and test system-level performance.
.

## Slide 111
Future evolution of Control Systems

## Slide 112: Modern Engineering Applications of Control
Flight Control Systems
  Modern commercial and military aircraft are “fly by wire”
  Autoland systems, unmanned aerial vehicles (UAVs) are already in place
Robotics
  High accuracy positioning for flexible manufacturing
  Remote environments: space, sea, non-invasive surgery, etc.
Chemical Process Control
  Regulation of flow rates, temperature, concentrations, etc.
  Long time scales, but only crude models of process
Communications and Networks
  Amplifiers and repeaters
  Congestion control of the Internet
  Power management for wireless communications
Automotive
  Engine control, transmission control, cruise control, climate control, etc
AND MANY MORE...

## Slide 113: Examples of Control Applications
Robotics:
  Robots perform automated tasks in assembly lines, where precision is important and dangerous tasks physically impossible for humans

## Slide 114: Aircraft Applications
Aircraft Flight Control
.• Stability augmentation
.• Configuration management
.• Maneuver enhancement
.• Maneuver limiting
.• Load alleviation
.• Structural mode control
.• Buffet alleviation (especially for twin-tail aircrafts)
.• Flutter margin augmentation

## Slide 115: Aerospace Applications
Control systems play a critical role in space flight

## Slide 116
Control systems in health

## Slide 117: Pharmaceutical Industry
Inventory
Recipe management
Packaging
Sampling
Tracking & tracing
Typical of batch processes

## Slide 118: Control Systems in Manufacturing

## Slide 119: For Substations
Protection (Lines, transformers, generators) very high speed response
control (remote or local) to guarantee power flow, safe operation (interlocking)
measurement (local and remote), electricity bill, power flow in grid

## Slide 120: Building Automation
basics: fire, intrusion, climate, energy management
HVAC = Heat, Ventilation and Cooling = air conditioning

## Slide 121: In Agriculture

## Slide 122: At Greenhouses
Humidifier System

## Slide 123: Feedback control is every where you just have to look for it

## Slide 124: End of the lecture Thanks for your attention